## WINDOM ANTENNA

I'm using homebrew Windom-Antenna recently.
In the total length of this antenna is 41m, height is about 11m, and diameter of element is 2mm.
However, it is up only about 4m height from a metallic roof.
I modified this antenna originally used as Inverted-V type of 80m band Dipole a little.
The feeding point of this antenna is located 13.6m from the edge of Element. Yes, it is Off-Centered.
BALUN of making which uses two cores, converts impedance into 1/4. The core is the one of about 4cm in the diameter. so there's no problem in the input power 100W at all. Because two cores are used, I think as much as 500W safe in power.

The diameter of the wire rolled in the core is about 1mm.

The VSWR to frequency is shown as follows.

| Freq. | VSWR | Freq. | VSWR | Freq. | VSWR | Freq. | VSWR |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3.525 | 1.1 | 14.050 | 1.8 | 18.070 | 3 | 28.150 | 2.5 |
| 3.570 | 1.4 | 14.100 | 1.7 | 18.160 | 3 | 28.500 | 2.0 |
| 3.795 | 1.6 | 14.150 | 1.6 | 21.050 | >3 | 29.000 | 1.3 |
| 7.030 | 1.4 | 14.200 | 1.3 | 21.449 | >3 | 29.300 | 1.1 |
| 7.060 | 1.3 | 14.349 | 1.2 | - | - | 29.600 | 1.2 |
| 7.099 | 1.2 | - | - | - | - | 29.699 | 1.3 |

In 21MHz, VSWR exceeds 3. However it is likely to QSO with the domestic area, if Antenna-Tuner is used. I did not obtain good results though I measured its VSWR with 10MHz and 24MHz besides <showing up>.
I think this easy structural wire antenna is Very FB. Because I can QRV on multi BANDs without switching some antennas.